## Slide 1: High Level Project Overview
Raw Field Data
Composite Work Cycle
Basic App Profile
Pre-Process
Data
Segment Data
Characterize Severity
Resolve Application
Low Level Data
Pre-processing Development
Severity Quantification Development
Data Seg Algorithm Modeling
Application Resolver Development
Composite Work Cycle: a reduced set of machine operations performed at some level of severity chosen to result in a machine experience that represents the desired portion (currently 90% severe) of the field population for design, simulation or validation of specific L4 and L5 systems.
Application Profile: a list of specific applications a machine or product performs, and the percentage of time spent doing each specific application.
…
…
Notes: Standard Definitions
·Operation: a relatively short, specific event or activity that a machine performs. Also referred to as a data segment, or operational segment. Example: dig, dump, load, carry, spread, rip, etc.
·Application: a relatively long, generalized task that encompasses one or more operations and describes the purpose for which the machine is being operated. Sometimes referred to as a cycle if the application is cyclical in nature. Example: production dozing, ripping, finish blading, stock-piling, etc.
·Application Profile: a list of specific applications a machine or product performs, and the percentage of time spent doing each specific application. Example: See the REDI “Machine Appl Prof” collection, and Caterpillar’s Business Intelligence Group’s database.
·Severity Characterization: a portrayal of how intense or acute an event was relative to the structural, kinematic, or dynamic physical response of an L4 system. If an operation is “what” the machine was doing, then severity is “how” it was performed. Severity can be measured or inferred in a variety of ways. Example: A dig event may incur a FELA value for a specific load of 200, a ripping event may incur a fatigue damage spectrum array with differing magnitudes for each frequency bin, etc.
·Composite Work Cycle: a reduced set of machine operations performed at some level of severity chosen to result in a machine experience that represents the desired portion (currently 90% severe) of the field population for design, simulation or validation of specific L4 and L5 systems. Operation information, along with severity characterization, is input for a composite work cycle. Example: See the REDI “Machine Appl Prof” collection, for example the CWC for D10T structures which includes 20% ripping, 5% travel ripped rock, 55% dozing ripped rock, and 20% pioneering.

## Slide 2: Classification: Supervised Learning Model
Training Data Values
Extracted /
Transformed
Features
Machine
Learning Algorithm
Labels
Predictive Model
New Data Values
Extracted /
Transformed
Features
Predicted Label
Classification: Place an unknown
object in a bucket of
knowns
Build the Model
Deploy the Model
Notes: SVM – Support Vector Machine
Currently Coded in Python

## Slide 3: Motor grader case study

## Slide 4
Version 1
Version 2
Version 3
Idle
Finish Blading
Heavy Blading
Ripping/Scarifying
Roading
Road Maintenance
Ditch Building
Ditch Cleaning
Snow Plowing
Snow Removal
Blade Slope Work
Side Slope Work
Travel*
Application Channel Development Approach

## Slide 5
95%
Goal
90%
80%
70%
60%
Snow Removal = 67%
Travel= 63%
Snow Plowing = 74%
Road Maintenance = 71%
Heavy Blading = 84%
Ripping/Scarifying= 84%
Roading= 88%
Idle= 97%
Finish Blading
Blade Slope Work
Side Slope Work
Ditch Cleaning
Ditch Building
Still Under development
Application Channel Results
SVM Predicted Application Accuracy

## Slide 6
Labeled
Micro Application – SVM Predicted Applications
Applications Labeled vs. Predicted

## Slide 7: ELECTRIC ROPE SHOVEL case study
Notes: Machine Overview:
Low Volume
High Productivity – 120 tons per pass
No Engine, all electric
Straightforward Cycle: Dig, Swing to Truck, Dump, Swing to Bank
Small amounts of movement (propel) between cycles. Max speed = 1 mile/hour